## Slide 1: 8Ke Paying for Energy
Do Now:
Make a list of things that use electricity in the photo. Number them from most electricity used to least
CW

## Slide 2
Equipment | Worksheets
 | 8Kd1 Power & Efficiency
Requisitions

## Slide 3: Objectives
  Recall that electricity and mains gas are charged for on the basis of the energy transferred.
  Explain why power companies use the kWh as a measure of energy.
  Recall some advantages of low energy appliances.
  Use data to consider cost efficiency by calculating payback times.

## Slide 4
Make a list of things that use electricity in the photo. Number them from most electricity used to least

## Slide 5
How is the spreadsheet calculating the energy?
What does the cost depend on?
What is the new, strange unit for energy?
Is electricity expensive?
Notes:  Click on the spreadsheet to estimate how much energy we use in a year and how much it costs.

## Slide 7
We pay for the amount energy we use at home, whether as gas (for heating) or electricity.
Energy companies use a unit called a _______-hour (kWh). (NOT “kilowatts per hour”)
Each kWh (often just called “_____” on electricity bills) costs about 15p.
kilowatt
Units
How did the spreadsheet calculate the energy?
So what is the equation for energy use (in kWh)?
Copy & Complete

## Slide 8
Example
How many kWh of energy are used if a 2 kW electric fire is on for 4 hours?
How much does this cost?
Start off the examples using QERNCU to set out your working in full.

## Slide 9
Example
How many kWh of energy are used if a 2 kW electric fire is on for 4 hours?
How much does this cost if each unit costs 15p?
E = ? P = 2 kW t = 4 h
E = Pt
= 2 kW × 4 h
= 8 kWh
cost = 8 × 15
= 120 p
= £1.20

## Slide 10
Use these power ratings to calculate the amount of energy used per day and the resulting cost for 3 appliances of your choice.
You can use the estimated times from the spreadsheet earlier or choose your own.
Set your working out in full using QE(R)NCU.
Cost per kWh = 15p
Check answers using spreadsheet

## Slide 11
Why is it better to use A+++ rating appliances?
Using more energy efficient appliances…
Why might it not be worth it?
Complete with the reasons, both for individuals and linking to the effect on climate change.

## Slide 12
Why is it better to use A+++ rating appliances?
Using more energy efficient appliances…
reduces the amount of energy we use, so i) costs less money ii) reduces the amount of fossil fuels burned. This means less CO2 is released and reduces our impact on climate change.
Why might it not be worth it?

## Slide 13
Payback time
Cavity wall insulation:
cost = £350 saving per year = £100 payback time = ?
= 3.5 years
Do you think this is worth it?

## Slide 14
 Calculate the payback time for each of these & write down your advice on which are worth it and which might not be.